## Slide 1: Multicycle Processor
Aaron Donawerth, Lucas Magasweran, Kevin Phan
5/9/11

## Slide 2: Introduction
What is a multicycle processor?
Why use a multicycle processor?
Datapath and controller of the multicycle processor
Performance of the multicycle
Verilog simulation of the multicycle

## Slide 3: What is the multicycle processor?
Processor that breaks an instruction into multiple steps and uses multiple cycles to execute.
Notes: TODO:include cycle comparison graph

## Slide 4: Why use a multicycle processor (trade-offs over single cycle)
Combined instruction memory and data memory
  Pros: Realistic, reduced chip size
  Cons: Single read port
Single ALU
  Pros: Fewer complex parts, cheaper, reduced chip size
  Cons: Needs non-architectural state registers and a finite state machine to share ALU
Faster clock
  Pro: Clock is determined by slowest step not slowest instruction

## Slide 5: Datapath and Controller

## Slide 6: Datapath and Controller
5 Step Process
  Fetch and PC increment
  Decode and register readout
  ALU Operation
  Memory Access/Register Write
  Register Write (lw)
Notes: At most 5 steps, at least 3 (e.g. j, beq)

## Slide 7: Datapath and Controller
Control Signals define the datapath
Datapath changes depending on the 3 type of instructions
  R-Type
  I-Type
  J-Type

## Slide 8: Controller Finite State Machine (FSM)
Notes: Review 5 step process, first two states are common because decode, example instruction

## Slide 9: Multicycle Performance

## Slide 10: Multicycle Performance
Performance is measured by Cycles Per Instruction (CPI)
CPI can be translated into Execution Time
Execution Time is
Notes: Movitvation for Multicycle,

## Slide 11: Multicycle Performance
Cycles per instruction
  Load Word = 5 Cycles
  Store Word = 4 Cycles
  R –Type = 4 Cycles
  Branch = 3 Cycles
  Jump = 3 Cycles
Notes: Main difference between Single Cycle!!!

## Slide 12: Multicycle Performance
SpecINT2000 Benchmark states
  25% loads
  10% stores
  11% branches
  2% jumps
  52% R-type instructions
Which comes to a CPI of 4.12 for Mutlicycle MIPS Processor

## Slide 13: Simulation